## Slide 1
Single Photon Detection:
Technologies & Applications
Emna AMRI
R&D Engineer at IDQ and PhD Student at GAP, Geneva University.
PROMIS Network second workshop: “Modelling and Design for Photonics”
Cadiz, May 18, 2016

## Slide 2: Progress up to date
Single Photon detection |  |  | 
 |  |  | Technologies
 |  |  | Applications for security

## Slide 3: Progress up to date
Single Photon detection |  |  |  |  |  | 
 |  |  |  |  |  | InGaAs/InP single photon detectors
 |  |  | Technologies |  |  | 
 |  |  |  |  |  | CMOS Single Photon Avalanche Diodes
 |  |  | Applications for security |  |  | 

## Slide 4: Progress up to date
Achievement:
Dark Count Rate (DCR) and After-Pulsing (AP) characterization of gated CMOS SPADs for Quantum Random Number Generation purpose.
Achievement:
Characterization of Free-running InGaAs/InP single photon avalanche detector with 50ps temporal jitter achieved at very low excess bias voltage.
Scientific output:
  A paper abstract was submitted and accepted to
SPIE 2016.
  A paper is being drafted and is to be submitted to Optics Letters (OSA).
Single Photon detection |  |  |  |  |  | 
 |  |  |  |  |  | InGaAs/InP single photon detectors
 |  |  | Technologies |  |  | 
 |  |  | Applications for security |  |  | 
 |  |  |  |  |  | CMOS Single Photon Avalanche Diodes

## Slide 5: Progress up to date
Single Photon detection
Technologies
Application for security
Quantum Random Number Generation
Exploiting randomness in
photon emission process.

## Slide 6: Progress up to date
Single Photon detection
Technologies
Application for security
Quantum Random Number Generation
CMOS SPADs Matrix
Quanta Image Sensor (QIS)
Achievement:
An entropy/bit of 0.9 has been obtained for raw data at room T for low bias voltage.
Scientific output:
A Poster was presented in DATE 2016 (Workshop on Trustworthy Manufacturing and Utilization of Secure Devices) March, Dresden-CH.
Block diagram of the QRNG
Schematic of a “jot” structure
Exploiting randomness in
photon emission process.
Achievement:
Generating randomness using a CMOS
6
image sensor with single photon detection capability and 200��𝟐 size pixels (jots).
Scientific output:
A paper was submitted to Special issue:
Photon counting image sensors and is
still in review.

## Slide 7: Future steps
Future steps:
  Finish the characterization measurements.
  Finalizing the paper writing.
  Prepare the talk for SPIE conference: “Optical Sensing, Imaging, and Photon Counting: Nanostructured and metamaterial Devices and Applications”, San Diego, 31 August 2016.
7
Single Photon detection |  |  |  |  |  | 
 |  |  |  |  |  | InGaAs/InP single photon detectors
 |  |  | Technologies |  |  | 
 |  |  | Applications for security |  |  | 
 |  |  |  |  |  | Others

## Slide 8: Future steps
8
Single Photon detection
Future steps:
  Co-integration of the SPADs matrix with post-processing digital blocks.
 Secondment in TU Delft for design review (end of Juin)
Technologies
Application for security
Quantum Random Number Generation
CMOS SPADs Matrix
Quanta Image Sensor (QIS)
Exploiting randomness in
photon emission process.
Future steps:
Co-filing a patent with Pr. Eric Fossum about QIS utilization for QRNG.
Investigate the possibility of using QIS for further applications such as optical instrumentation.

## Slide 9: Conclusion
Progress:
The project has been well progressing thanks to the collaboration of the engineers in IDQ and the scientists in the GAP.
Secondments:
Group of Applied Physics: Quantum Technologies: A PhD work during 3 years.
TU Delft: scheduled for end of Juin.
Looking forward to constructive exchanges with other ESRs that may lead to fruitful collaborations.