## Slide 1
WP 2 Materials for Security : Overview - ESR 5, 6, 7 & 8
Collaborating Partners: SGENIA, ROME, ULANC, NOTT, Tyndall-UCC, IDQ, NAsP
Objectives: To improve performance sensitivity of imaging systems by developing novel APDs and SPADs with nanometre wide avalanche regions; To improve infrared materials using improved buffer technology
IDQ
Specify specs, test SPADs for QKD
SGENIA
Photon starved applications, LIDAR, optical comms
NAsP and UMR
MOVPE growth?
Cadiz
Characterisation
TEM
Rome - Hydrogenation
ESR 5 – SHEFF
Nanometre wide avalanche regions for high performance single photon avalanche diodes (SPADs).
ESR 6 - Tyndall-UCC
Time-resolved characterisation of narrow gap semiconductors
ESR 7 - SGENIA
Development and device applications of APDs for operation in photon-starved regime
ESR 8- SHEFF
APDs with ultra-thin avalanche region for sensitive X-ray detection.

## Slide 2
Aim
Design Single Photon Avalanche Diode (SPAD) with nm avalanche region.
Plan
Simulation of field profile and avalanche gain
MBE growth of wafers
Extraction of parameters
Improve design and growth
Device processing
Device testing I-V-T, Quantum efficiency
Breakdown characterisation
WP 2: ESR 5
Nanometre wide avalanche regions for high performance single photon avalanche diodes (SPADs).
Supervisor: Prof. C. H Tan; Collaborating Partners: IDQ, SGENIA, UCA, Tyndall-UCC
Partners
IDQ - cross check SPAD characteristics, QKD
SGENIA - test SPADs for free space optical comm. integrate plasmonic lens
UCA – TEM
Tyndall – lifetime study
Status
ESR recruitment delayed. Aim to start mid-Oct.
AlGaAsSb pin and nip diodes grown.

## Slide 3
Materials | E (eV) | EL(eV) | EX(eV)
InP | 1.35 | 2.05 | 2.21
In0.52A0.48lAs | 1.45 | 1.69 | 1.74
AlAs0.56Sb0.44 | 2.39 | 2.18 | 1.85
InP
InAlAs
AlAsSb (Mmix)
Very low excess noise, and very small temperature coefficient of breakdown
-Investigate use of AlGaAsSb, to find the optimised bandgap to achieve low noise, good breakdown characteristics and optimised field profile.
Excess noise reduces in thin layers

## Slide 4
WP2 Materials for Security: ESR 6
Time-resolved characterisation of narrow gap semiconductors
Supervisor: Dr. Guillaume Huyet / Dr. Tomasz Ochalski
Offer made and accepted by Ms. Shumithira Gandan (Malaysia)
  B.Eng. (Hons) Electrical & Electronic Eng.
  M. Eng. In Photonics – Application of Photonic Crystal Fiber in Thulium-doped Fibre Amplifier
  Industry experience – Fujitsu and Telekom Malaysia
Some delays due to paperwork (CIT/Tyndall double bureaucracy!)
  Should be in place early Oct
Project nominally in WP2, but can probably contribute across all WPs.

## Slide 5
Composition tuning – TRPL of composition dependent lifetime
e.g. Nanopillars: GaAs/InGaAs core, GaP shell
1.7 ns
0.6 ns
0.085 ns
τ:
x=0.08
x=0.15
x=0.26
Wavelength (nm)
Strain-induced non-radiative recombination
Should be applicable to defects in APD layers
Increasing strain

## Slide 6
GaAsN/GaAs hydrogenated QDs preliminary results
  samples from Rome
GaSb/GaAs QDs
  Experience working with Sb-based QDs on GaAs substrates
  Possible quality check for samples on GaAs and Si substrates
60 meV
shift
Extremely large span
150+ nm
Plan for single-dot PL
Would be useful to compare TRPL for different sizes and geometries of GaAsN QDs – samples needed!

## Slide 7
WP2 Materials for Security: ESR7
Development and device applications of APDS for operation in photon starved regime
Supervisor: Prof. J. L. Pau and Dr C Rivera
Flavio Nucciarelli
PhD student
SGENIA & Universidad Autónoma de Madrid
Aims:
Develop array of APDs/SPADs
Incorporate plasmonic and photonic crystal-like structures will be studied to add functionality in terms of spectral selectivity and optical coupling.

## Slide 8
SPP LENS
APD
2 mm
3 – 4 mm
APD
150 μm
150 μm
20 μm
Improving collection efficency APD device

## Slide 9
High numerical aperture (NA) at a specific λ
Increasing sensor detection area without noise increase
Processability and integration are simplified compared to optical lenses
Acting on polarization and phase of the incident wave
Benefits in using Plasmonic lens in SPADs
APD
M
E
T
A
L
E
N
S
x 10-100

## Slide 10
Hole array lens
Example structure: r =140 μm and
t= 19,08 μm @ λ=10.6 μm
Key features
f focal length
r lens radius
L hole arrays period
a hole dimension
t thickness
Die dielectric material
Me metal material

## Slide 11
Aim
Avalanche Photodiodes with thin avalanche region for X-ray detection
Plan
Simulation of field profile and avalanche gain
MBE growth of wafers
Extraction of parameters
Improve design and growth
Device processing
Device testing I-V-T, Quantum efficiency
X-ray energy resolution measurements
WP 2: ESR 8
Nanometre wide avalanche regions for high performance single photon avalanche diodes (SPADs).
Supervisor: Prof. C. H Tan; Collaborating Partners: SGENIA, UCA, Tyndall-UCC, UAM, NAsP
Partners
SGENIA - test APDs, amplifier and signal processing (placement)
UCA – TEM
Tyndall – theoretical modelling and TRPL (placement)
NAsP – MOVPE (placement)
Status
ESR started in Sept.
ESR undergoing training
AlGaAsSb pin and nip diodes grown.

## Slide 12
Combine good absorption characteristics of InGaAs, with a very thin avalanche region to improve the FWHM of soft X-ray detectors.
Gain fluctuation decreases when more carriers initiate the avalanche process- Central Limit Theorem
Avalanche gain reduce the effects of electronic noise